## Slide 1: Waste Management IOT Project
Sensors to be used

## Slide 2: Measurement needs
Real time GPS position of bin
Fullness of each bin
Air quality around bin
Real time GPS position of skoupidiariko

## Slide 3: Bin/Skoupidiariko position
Suggested option: LORAWAN Micro GPS Activity Tracker
Features
  Battery powered (up to 3 years)
  Configurable frequency
  Also indoor via sniffing of WIFI networks (WIFI triangulation)
  15 km range
  Temp. range -40 / +85°C

## Slide 4: Bin Fullness
Suggested option : SENSONEO ultrasonic sensor
Features:
  Measuring range: 3-170 cm
  LoRaWan connectivity
  Measurement 24 times a day
  Temp. Measurement
  Integrated accelerometer
    Emptying recognition
    Has fallen recognition  reward citizens if they fix it
  Replaceable Batteries  reward citizens if they replace them

## Slide 5: Air quality around bin
Suggested option : Envitus LoRaWAN® Outdoor Air Quality Monitor
Features:
  Temperature
  Humidity
  O3,CO,SO2
  Pressure
  NO2